## Slide 1: Radio Receiver Andrei Vasilev and Joshua Sevick

## Slide 2: Receiver goals
Frequency Range 3.5 – 14.5 MHz
Tayloe mixer
Gain of 5
SSB reception, HAM radio use

## Slide 3: Schematic* 01
Corrected to account for the wrong pinout

## Slide 5: Key features
No transformer
Band pass filter
  Hand wound (winded) inductors
Tayloe mixer
Test points for tracking down bugs
Sensitivity down to 1 uV

## Slide 6: Initial Struggles
Mistaken parts
  74HC4052 didn’t meet frequency spec
  Op-amp: NE5532 wasn’t rail to rail
  ChatGPT led us astray
  With the help of Dr. Frohne, SN74CBT3253 and TLV2172IDR were chosen

## Slide 7: 02
Board Layout*
Reflects how the board actually is

## Slide 9: Struggles
Incorrect initial pin assignment
  Online footprint for the op amp had the second op amp inputs reversed
  Ended up having positive feedback instead of negative
  Led to saturated op amp
0, 90, 180, and 270 degree phases were summed wrong
  Instead of the difference between 0 and 180 and 90 and 270, it was the difference between 0 and 90 and 90 and 270
Led to bad image rejection

## Slide 10: Fixes
Drill baby drill!
  Drilled into the traces to sever the connections
Hand soldered connections
  Using the test points as pad connections
Image rejection fix
  Band pass filter was interfering with the input signal
  Bypassed the bandpass filter to get cleaner signal.
    Achieved better image rejection at 1 uV

## Slide 11: Hardware 03
Signal strength, hardware fixes, and image rejection

## Slide 13: At 1 uV

## Slide 14: At 3 uV

## Slide 15: At 1 mV

## Slide 16: 3-Fold Problem
The 1:4 MUX was wired for a binary clock instead of I2C.
  Wired for 0, 1, 2 ,3 instead of 0, 1, 3, 2.
Incorrect phase summing
  0/90 degrees phase summation 180/270 phase difference
Incorrect schematic footprint.
  The datasheet revealed that we had positive feedback instead of negative.
  The positive and negative terminals were reversed

## Slide 17: Room for improvement
Image rejection becomes flawed at louder signals
        Quisk image rejection could not be figured out and implemented
        Hardware was faulty. We should have spent more time reviewing our design before we printed it